## Slide 1: Experimental Study of Solitary Wave Evolution over A 3D Shallow Shelf
Patrick Lynett, David Swigler, Sangyoung Son, Duncan Bryant, Scott Socolofsky
Coastal and Ocean Division, Zachry Department of Civil Engineering

## Slide 2
Purpose
Limited available experimental data to compare numerical models with the nearshore, turbulent dynamics of a nonlinear long wave
Need for a 3D tsunami-like dataset, with turbulence measurements

## Slide 3: Experiment#1 Setup
Basin:
48.8m x 26.5m x 2.1m
Piston-type wavemaker
Bridge spanning width
of basin
Complex shelf
Planar beach
Water depth: 0.78m

## Slide 4: Instrument Layout
: 21 acoustic-Doppler velocimeter (ADV) array locations
: 275 wave gauge (WG) locations
: 45 ultra-sonic wave gauge (usWG) locations

## Slide 5: Experiment Procedure
Generated a single solitary wave (H=0.39m, depth=0.78m) for each trial
Trial consisted of a 45 second timeseries beginning w/ wave generation
20 trials for each ADV location
2 trials for each WG & usWG location

## Slide 6: Experiment#1 Setup

## Slide 7: Experiment#1 Setup

## Slide 8: Basin Hydrodynamics
http://ceprofs.tamu.edu/plynett/isec/Movie_Dye.wmv

## Slide 9: Basin Hydrodynamics – WG Data

## Slide 10: Max Free Surface Elevation
Shoaling
  Negligible offshore and at shelf apex
  Significant near basin side wall
Breaking
  Rapid decay in wave height near shelf edge
  Continued as Borefront (1) propagated shoreward

## Slide 11: Refraction
Dye revealed
  Pathlines behind leading wave
  Enhanced mixing within the front
Refraction due to bathymetry of shelf
  Directed toward centerline of basin
  Not particularly evident in the breaking front
  Very clear in the following onshore flow

## Slide 12: Wave Runup
Nonuniform in longshore direction due to refraction
@ X=29m: arrives first near basin side wall
@ X=39m: arrives first along basin centerline
http://ceprofs.tamu.edu/plynett/isec/Movie_Runup.wmv

## Slide 13: Wave Runup
Greatest cross-shore velocity along centerline due to jetting mechanism
Forcing causing convergence relaxed
Mass of water spread laterally and shoreward
http://ceprofs.tamu.edu/plynett/isec/Movie_Runup.wmv

## Slide 14: Kinematics @ Shelf Apex
http://ceprofs.tamu.edu/plynett/isec/Movie4.wmv
All values in cm/s

## Slide 15: Turbulent Energy @ (X=13,Y=0)
All values in cm/s

## Slide 16: Turbulent Energy @ (X=13,Y=0)
All values in cm/s

## Slide 17: Coherent Structure
Green dye reveals eddy
Flow directed away from centerline @ 27s due to eddy’s arrival
Flow directed toward centerline starting @ 29s after the eddy’s center passes
Increased turbulent energy after 26s due to eddy
http://ceprofs.tamu.edu/plynett/isec/Movie8.wmv

## Slide 18: Experiment #2: Bottom Layout
Add a bump to the apex of the shelf

## Slide 19: Future Work – This Summer
Add a bump to the apex of the shelf
http://ceprofs.tamu.edu/plynett/isec/P_NEEStsunamos3.E_DyeStudy.T_Trial06.cam11.avi

## Slide 20: Second Experiment – Add Obstacle
Surface PIV Study
  20 gallons of 2.5 mm D, 0.9 S plastic spheres
  Camera mounted on bridge, looking down
  10 overlapping FOV’s

## Slide 21: Second Experiment – Add Obstacle
Add a bump to the apex of the shelf

## Slide 22
Transient long waves undergo complex processes in shallow water
Nonlinear, turbulent
“Single” incoming wave quickly leads to numerous waves
Developing models at the same time, these are experiments necessary to validate them
Nearshore Dynamics of Long Waves
Many thanks to the staff at OSU – Tim Maddux, Sungwon Shin, Linda Fayler, Jason Killian

## Slide 23: Repeatability
WGs closest to wavemaker (along X=5m)
Total of 28 trials overlaid
Measured wave height between 0.36m-0.38m
Solitary wave @ 1.3s
Trough @ 3.0s
Secondary wave @ 3.8s

## Slide 24: ADV Filtering
Filter 1: SNR > 10 decibels
Filter 2: COR > 70%
Filter 3: Curvature
  Shoreward of shelf edge: <300 m/s3
  Offshore of shelf edge: <175 m/s3
Filter 4: ≥ 10 trials to quantify turbulence